## Slide 1: Multi-objective optimization for crashworthiness design of vehicles
Project
Name: Banderwaar Akshay Sai

## Slide 2: Optimization problem formulation
The goal of this project is to design the thickness of five reinforced members around the frontal structure of a vehicle, taking into account (1) the overall weight of the vehicle, (2) toe board intrusion and (3) acceleration-induced biomechanical damage of occupants in a frontal crash.
such that:

## Slide 3: Proposed combination’s
GP Model + Constrained Expected Improvement
GP Model + Constrained Probability of Improvement
GP Model + Probability of Improvement + One pass Penalty
GP Model + Expected Improvement + General Exterior Penalty (with adaptive weight sampling)
(GP Model + RBF + Decision Tree) + Constrained Expected Improvement

## Slide 4: General procedure
Step 1. Pre-processing (normalize design variables; dimensionality reduction by the Morris method)
Step 2. Sample initial solution candidates via LHS design
Step 3. Evaluate solutions using the expensive objective functions to form training data
Step 4. Randomly pick subproblem (weights ) and form aggregated dataset
Step 5. Train a surrogate model using
Step 6. Use the surrogate model to get a new infill point corresponding to the selected single-objective subproblem
Step 7. Evaluate to get and append to the training dataset:
Step 8. Return to Step 4 if solution evaluation budget not exhausted
Step 9. Return the set of nondominated solutions found in

## Slide 5: Weight sampling
Random sampling from [0,1]
Generate weights evenly spaced between 0 and 1 (= linspace(0,1,N) and = 1- )
Adaptive weight sampling (based on gap angles)

## Slide 6: Adaptive weight Sampling- (Angle-Based Gap Detection)
In bi-objective space, every normalized point ​ =(​, ​ ​) corresponds to the direction.
Convert each point to an angle:
Add boundary angles 0,90
Find the largest angular gap
The midpoint of this empty interval gives the least explored search direction.

## Slide 7: Deriving Weight w From Desired angle
Relating Angle to Weighted Sum
Since the line corresponding to the midpoint angle satisfies the objective function, its slope is =. The slope corresponding to the average angle is and we know that = -1.
After solving, we obtain:

## Slide 8: Limitations and improvements
Due to it’s simplicity, it is too sensitive to outliers.
One small improvement to this naïve method is that we mark the dominated arc with respect to an ideal point outside the region, so we do not consider those point. (introduces hyperparameter)
we train model using random Weights until some fixed
number of iterations so that by that time we get a good
approx. pareto optimal points then we adopt adaptive
sampling using these pareto points.

## Slide 9: GP Model + Constrained Expected Improvement (Algo-1)
Methodology:
1. Initial Sampling
Generate m = 11d - 1 points using maximin LHS in
Get the objective function values ,
Define constraint as g(x) = 5 - (x). ( such that g(x) >=0)
2. Surrogate models
Constraint GP (always trained on full dataset)
  Train GP on g(x) .
Objective GP (feasible or full dataset )
  Normalize , to [0,1] using Minimax and define single objective: = w + (1-w)
  Train GP on

## Slide 10
3. Acquisition Function
if no feasible point available then we maximize the probability of feasibility P(g>=0)=(/ ).
Else maximize Constraint Expected Improvement (cEI)
  cEI(x) = EI(x). P(g() >= 0)
4. Acquisition Optimization
Use Simulated Annealing to maximize acquisition and obtain
5. Sequential Update
Evaluate and push it in dataset and repat whole process again until u exhaust total budget.

## Slide 11: GP Model + Constrained Probability of Improvement
Same Framework as Algorithm 1
LHS sampling to generate initial points
Objective and constraint GP surrogate construction.
Acquisition optimization using Probability of Improvement (PI) × feasibility
Optimization via Simulated Annealing
Sequential updates for 200 total evaluations

## Slide 12: GP Model + Probability of Improvement + One pass Penalty
Same Framework as Algorithm 1
LHS sampling to generate initial points
Objective and constraint GP surrogate construction.
Acquisition optimization using Probability of Improvement (PI) × feasibility
Optimization via Simulated Annealing
Sequential updates for 200 total evaluations

## Slide 13: GP Model + Expected Improvement + General Exterior Penalty
Same Framework as Algorithm 1
LHS sampling to generate initial points
Objective and constraint GP surrogate construction.
Acquisition optimization using expected Improvement (infill criterian) and (constraint handling) General exterior penalty
Optimization via Simulated Annealing
Sequential updates for 200 total evaluations

## Slide 14: (GP Model + RBF + Decision Tree) + Constrained Expected Improvement
Same Framework as Algorithm 1
LHS sampling to generate initial points
Objective and constraint GP , RBF , Decision Tree surrogate construction.
Acquisition optimization using Probability of Improvement (infill criterian) and Onepass exterior penalty (constraint handling)
Optimization via Simulated Annealing
Sequential updates for 200 total evaluations

## Slide 15: Results and Plots obtained
 | GP+EI const (IGD - avg over 10 runs) | GP+PI const | GP+PI+One pass | GP+ EI+ external penalty | GP+RBF+Decision Tree + external penalty
Random weight initialization | 0.04406 | 0.04396 | 0.04097 | 0.04346 | 0.07341
Naïve Adaptive sampling | 0.11054 | 0.08823 | 0.07297 | 0.10015 | 0.07518
Improved Adaptive Sampling | 0.05339 | 0.05314 | 0.0474 | 0.0512 | 0.07926
Inverted generational distance comparison

## Slide 16
M1
M2
best
worst

## Slide 17
M3
M4
best
worst

## Slide 18
M5
best
worst

## Slide 19
THANK YOU